## Slide 1
Check Sheet
Problem
How to capture data for analysis?
Define the data needed to address a specific issue.
Choose an appropriate check sheet style, such as
  Obtaining the distribution of a specific item
  Counting the number of defective items
  Identifying where defects occur
Create the check sheet.
Train the team on how to use the check sheet.
  Test the team and the check sheet to ensure the data captured is correct and useful.
Determine how, when, and where to collect data.
Collect the data.
Check Sheet Process
Existing process
Team
Check Sheet
Data for analysis
Difficulty
Easy to use
Copyright © 2022-2023 Dan Zwillinger. All rights reserved.
A Check Sheet is the simplest quality tool.
A check sheet is an organized way to capture information.
The information captured can be quantitative or qualitative. When quantitative, a check sheet is called a tally sheet.
Each type of check sheet has a different purpose, such as:
  Counting number of defects
  Determining defect locations
  Determining how defective something is.

## Slide 2
Check Sheet – Several Examples
Copyright © 2022-2023 Dan Zwillinger. All rights reserved.
Obtaining the distribution of an item
https://commons.wikimedia.org/wiki/File:GAZ-24_Volga.svg
Counting defective items
Defect location

## Slide 3
Check Sheet – Notes
Slide 1
Slide 2
Each check sheet is designed to meet a specific need; there is no standard format.
A check sheet is not a checklist.
Check sheets are used to either gather data for subsequent analysis, or to support conclusions already obtained.
A well-defined check sheet reduces the chance that different people will collect data in different ways.
Potential failure modes of check sheets:
  Making the check sheet too complicated
  Not allowing operators enough time to capture all relevant information.
  Not piloting or testing the check sheet before large scale deployment.
  Obtaining data that will not be used.
  Poor definitions of how to obtain data, resulting in missed or noisy data.
A Check Sheet is one of the “7 Basic Quality Tools”: Check sheet, Control chart, Divide and Conquer, Fishbone diagram, Histogram, Pareto chart, Scatter diagram.
The examples show the three major types of check sheets.
Top left – distribution – this data is ready to be made into a histogram.
Top right – counts – this data is ready to be used in a Pareto analysis.
Copyright © 2022-2023 Dan Zwillinger. All rights reserved.